Silver Pro user's manual

Table of contents:
    1. Useful information
    2. Getting to know your Silver Pro
    3. Features
    4. Water and recommendations
    5. Probes and connections
    6. Powering up the Silver Pro
    7. Making your first batch of Ionic Colloidal Silver
    8. Do's and don'ts
    9. Miscellaneous
    10.

Section One:

        Useful information

Here we will include some information that maybe useful for you.

It is advisable to make your ionic colloidal silver solutions in some type of laboratory flask. It is also advisable to get some type of magnetic stirrer to stir the
solution during its processing time.

If you go this route, you can use a rubber stopper to hold the probes in the solution.
The clips that are connected to the probes can never touch the solution and you are making sure no contaminates from the surrounding environment never get into the solution.

The silver pro can be ran from as little as 9.0 v dc but, will operate in a diminished
capacity. IE., it will take longer to get the process completed.

You can search the internet for some pretty decent lab equipment, Flasks, magnetic stirrer, silver probes etc. There is quite a supply of this stuff on eBay...
One note is to make sure you get your silver from some place you can trust!

Never use an aquarium air pump (or anything of that nature) to stir your solution with. You will be taking all of the dust,pollen etc,etc and putting that right into your cs solution!

If you are going to make large batches (the Silver pro will accommodate this) say like 5 gallons at a time, use a 5 gallon container with a lid on it ! Also you can place a pump into the container to circulate the water. The silver Pro can supply up to 200ma. Of current, and even more with the right power supply. Up to 1.5 amps of current can be supplied if your power supply can handle it. That means you can make a serious amount of CS solution if needed to.

Just remember to keep your current levels to .001 ma of current per sq inch of the probes surface area.

Another note: Never let your solution come into contact with any metal of any type. This will strip the + charge from the ions and the solution will be useless!

Storage of the colloidal silver should be in glass bottles not plastic. Wine bottles with the cork work very well indeed.

Section Two:

        Getting to know your Silver Pro

     2.1 Silver Pro casing
     2.2 Mode led's 1-4
     2.3 Operation push buttons
     2.4 Polarity led
     2.5 Constant current/Constant voltage led
     2.6 Banana jacks/Binding posts
     2.7 Parts per million/Current potentiometer
     2.8 Front air exhaust vent
     2.9 Master power switch
     2.10 Power jack/cord
     2.11 Rear fan air intake vent

1. Silver Pro aluminum casing: Casing should be cleaned with a damp cloth only. Do not pour water on or rinse this unit, it's not water proof.
2. Mode Led's: Starting from let to right (rear to front) mode #1, mode #2,
  mode #3 and mode #4 led's. These leds indicate what mode you are currently
  in. (Except while in progress mode)
3. Operation push buttons: Starting from let to right (rear to front)
  Mode selection button, Start/Pause button, Custom current selection and
  Reset button.
4. Polarity indicator led: This led indicates the state of the polarity the Silver Pro is currently producing. (positive/negative)
5. Constant Current/Constant voltage led: This led indicates the state of the
  Silver Pro's constant current/voltage mode.
6. Banana jacks/Binding posts: This is the Silver pro's output connection to
  the silver solution. (electrical load)
7. Parts per million/Current potentiometer: This is the Silver Pro's parts per
  million set point setting and in custom mode, it is also the custom current
  set point setting.
8. Front air exhaust vent: The Silver Pro's air exhaust vent.

Section Two:

      9. Master power switch: This is the master on/off switch. (power switch)
    10. Power jack/cord: This is where you plug in the power supply unit.
        Max voltage is 30.0 V dc Center pin is positive with respect to ground.
    11. Rear fan air intake vent: The Silver Pro's rear fan air intake, please
        take care in keeping it free from obstructions.

Section Three:

        Features

     The features on the Silver Pro are many, we will list them here.

1. A good strong sturdy aluminum case, will provide you with years of satisfactory service.
2. Easy push button controls, very easy on the fingers.
3. Four modes of operation to choose from via a single push button.
4. Constant current regulation down to the pico amp range.
5. Custom mode (mode four) is selected via push button and offers you from
  .001 to .200 ma of current. (use any probes you want to)
6. Short circuit detection and self restart. (up to three times) after the third time
  the Silver Pro will halt the process and wait for you to restart it.
7. A pizo element (sounder) that will audibly inform you of a short circuit condition, start condition and It also plays a tune at the completion of your solution.
8. Visual progress bar, after one minute of operation and no buttons are pressed
  during that time, the Silver Pro will enable the progress bar display.
  This display monitors how far along you are in 25% increments. It does this
  with the use of the four mode leds. When all four are lit for a time period of
  One minute, the process will complete.
9. Completion indication happens when all four mode led's stay on for a duration
  of one minute, after the Silver Pro completes its solution ppm setting, it will
  scroll the mode leds until a new start command is issued by the user.
10. Closed loop live current monitoring system allows for very fast current corrections and much better control of the current loop.
11. On board AVR an Atmel Atmega8 running at 8 MHz has complete control of
        of the process at all times, it is constantly updating the process keeping it all
        under control, so you don't have to.
Polarity reversing keeps the probes clean so you don't have to. Without it, you
        would have to clean the probes about once per hour. This will help to free you
        up so you can get on with whatever it is that you do.
     13. Set it and forget it, push a button to select your operating mode, set your ppm
        setting (if not already set) start it and walk away, its that simple.
     14. Top cover led indicators (six in total) provide an easy visual indication of the
        entire operation process at all times.
     15. A Pause button with led flashing indicator, this is an easy way to pause the
        process while it is running, press again to resume.

Section Four:

        Water and recommendations

For water it is of the utmost importance that you only use distilled water for your ionic colloidal silver solutions. Anything else carries a very high risk that you may pollute your solutions to the point that they could cause harm to you.

You also need to take great care in the selection of the silver probes that you are going to use to make your solution. The lowest quality silver that you should use should be no less than .999 silver. We do recommend .9999 for the probes though.
Any thing less than .999 you run the same risk as using bad water, except with the
probes you run the risk of heavy metal poisoning as you have no idea what is in that
silver, you surely don't want to use it!

Additives should never be added to the water! Once again, please make sure the
water you use to make your solution is only distilled water. Never add anything to the water itself. If you want to enhance the waters conductivity for a faster processing time, use some solution from the last batch.

If you don't have a last batch to seed the new batch with (such as in your first batch) then you will have to wait the extra time required to complete the current cs solution.

Try not to make high ppm solutions, usually 10 to 20 ppm is sufficient enough for any situation. Making higher concentrations is possible, but take much longer to complete. IE. A 30 ppm solution with One once of seed takes about 12 hours to complete. Without seed, could take up to 16 hours or more!

40 to 45 ppm even with a seeded starting batch will be at least 24+ hours.

So you can see, the stronger it is the more time it takes to make this.

These calculated times are based on mode 2 at .004 ma of current flow. Mode 3 could be used to make it slightly faster. The trade off will be the size of the silver ion will be increased slightly.

Section Five:

        Probes and connections

The probes can be about any thing you can find that is at a minimum at least
.999 silver. (nothing less is acceptable)

Try to find something that offers a larger surface area and extends at least 50% of
the way into the solution. If nothing can be purchased, you could use some old silver
dollar coins and mode 4 to set the correct amount of current.

In a normal situation you will be using some type of silver strips or long rods.
Rod shaped is usable but not preferred as the curved shape prevents optimum surface
area current transfer.

The idea probe would be at a minimum 5mm wide by as long as you can get in the
flask (almost touching the bottom) and a least a few mm thick.

The more surface area you can get, the faster you can make the CS Solution.

Probe connections: The Silver Pro offers banana jacks and binding post for the connection to the probes. From that connection it is preferred to use some type of
alligator clips to connect to the probes.

Power supply’s usually have these types of wiring, with banana type plugs on one
end and alligator clips on the other end. These can be purchased pretty cheaply and
readily available.

Just make sure that no matter what setup you choose to employ to make your CS Solution, that the only thing that touches the water is just the silver probes. No part of the clips or wire should be in the solution at any point in time.

Section Six:

        Powering up the Silver Pro

To power up the Silver Pro, all that needs to be done is plug in the power supply to
the Silver Pro itself.

Follow these steps:

1. make sure the power supply you are going to use is off, then make sure the Silver Pro's master power switch is in the off position.
2. Plug in the power supply output (plug) into the back of the Silver Pro's power jack. (making sure the center pin is +)
        The Silver Pro is protected against reversed power supply connections, should
        It happen, it should not cause a problem.
  1. Plug in your power supply or switch it on, then proceed to turn on the master power switch on the Silver pro.
  2. At this point power should be on, and the mode 2 led should be lit up.
    Also the CC/CV led may also be lit up.
  3. If this is the case, the Silver Pro is now ready for use.

Section Seven:

        Making your first batch of Ionic Colloidal Silver

So, you made it this far, now is the time to reap your rewards as we are going to actually make some colloidal silver.

For this we will use the flask and the magnetic stirrer. Make sure the flask is clean!
You may use soap of some type to clean it with, just rinse it well. Even after you rinse it, it will still be contaminated by the rinse water!

You must rinse it first then rinse it with the distilled water at least three times.

It is highly recommended that you purchase a PWT that measures in micro Siemens.
How else will you know the strength of your solution. Hanna PWT (pure water tester)
is one that is ideal for this. A TDS meter will work, but is not very accurate.

I highly recommend the Hanna PWT, as this is exactly what it was made for. And it
measures right down to the low scale where most of your solutions will be at.

Place your flask on the magnetic stirrer, fill it with distilled water, before you add the stirring bar, rinse it too, with the distilled water.

Add the stirring bar to the flask. Set your probes and rubber stopper setup into the top of the flask. Check the water level against the probes and stopper. You want about 1/8 of an inch of space between the water level and the rubber stopper.

Once this is correct, turn on the magnetic stirrer. Set the speed of the stirrer to just produce a small dip at the top water level in the flask. We are now ready to start the process.

Turn on the Silver Pro, mode 2 should show up by default. Connect the Silver Pro to the two silver probes protruding from the top of the rubber stopper in the flask.

Press the start button on the Silver Pro, the polarity LED will lite up, power is now being supplied to the cs solution. It is not making the solution at this time, it is performing a test on the water in the flask. When this test completes the Silver Pro
will do one of two things, either start the process (by beeping two short tone bursts)
or fail the water test.

If you get the two short beep tones, the process is now started and running.
If it did not start, then the water is not usable for quality CS. You can still use this water for cleaning or topical usage but do not consume it!

Section Seven:

        Making your first batch of Ionic Colloidal Silver

If the Silver pro did not start the process, you can still start it manually.
Remove the connections from the Silver Pro's banana jacks. Press the start button again. It will start the water test again, this time it will pass and start the process.

Once you get the two short beeps, then just plug in the probes again. Pay attention when you do this, when the probes get inserted into the Silver Pro while the process
is started and the water is dirty (not clean) it may present a large current draw, over the limit of the internal set point. When this happens the Silver Pro will set the current to a very low setting, produce 4 long beep tones and then try to restart.

Chances are good that it will restart with no problems. The reason for this is that when the process is running it's trying to hold itself at the selected current setting, So the Silver Pro will raise the voltage to it's highest point to try to achieve this current setting. With the voltage up all the way, and you place the connection to the load (cs solution) it may draw more current than that mode is allowed to draw.

When this happens the Silver Pro will see that something is wrong and possibly a shorted condition may exist. So the Silver Pro will set every thing to a very low setting and proceed to test for a shorted condition. If no short is found, it will resume the process.

Now that the process is running, go do something else. You do not need to baby sit
this generator.

After a few hours time you will notice that the Constant current/Constant voltage led is now or already has changed to the Constant current mode.(red led)

This is normal and is just a visual indication that the Silver Pro is now limiting the amount of current you solution can draw, per the mode you are in. (mode 2 at this time)

The progress display should also be active and indicating the percentage of completion it is now currently at. It uses the mode leds for this purpose.

You will see either mode 1 led, mode 2 led, mode 3 led and possibly mode 4 led.
Each led represents 25% completion, so if you had mode 1, mode 2, and mode 3 leds lit, that would indicate that you are 75% complete. This is based off of the parts per million set point on the front panel. The higher it's set point, the longer it will take to complete.

Section Seven:

        Making your first batch of Ionic Colloidal Silver

As the silver pro works towards it's goal, sometimes you may hear a 4 tone burst.
This indicates that a short has occurred The Silver Pro will try to clear this condition
if it exists. Shorts sometimes happen, if the probes should get bridged from an oxide
condition. (rarely happens) When this does occur, the Silver pro will normally clear it
on the next current reversal. You would never have known it occurred if you had not heard the beeps!

At some point in time, the process will hit the required ppm set point and be ready to be stopped. The Silver Pro will monitor this end of the process. When it comes time for completion you will notice that the progress bar display now has all mode leds lit up. (100% completion) In order for the Silver Pro to complete the process, all 4 mode leds must be lit up for a 1 minute time duration. If one led (mode 4 mostly) should as
much as even blink, the timer will restart from zero again and repeat this until all four
leds will remain lit with no blinks for a 1 minute stretch of time.

This helps the Silver Pro to have very repeatable results over and over again. Usually
within 1 ppm per batch.

When the process has completed, the Silver Pro will enter into a scroll mode of operation. This means after completion the Silver pro will turn all voltage off
and just sit there and scroll the mode leds left to right until, you either start a new batch or you just turn it off.

A quick note: At any point in time while the Silver pro is running, you can pause the process by pressing the start button again, while paused it will flash the current mode led just to let you know it is paused.

Why would you want to pause it you may ask? There are times you will want to take a measurement of the parts per million while it is running, the pause feature allows this without having to restart everything over. (water test) When done doing what you needed to do, just press the start button again and the Silver Pro will resume from
where it left off.

OK now that you have the first batch completed leave the Silver Pro in the on state.
(with the leds still scrolling across) From here you have two choices, shut if off or make a new batch.

If you have another flask ready you can fill it up and get started again, this time using

 Section Seven:

        Making your first batch of Ionic Colloidal Silver

some solution from the first batch you just ran. (seeding)

This is called seeding and it cuts the process time almost in half! To do this you must
use about 1 to 2 ounces of the first batch in the second batch you start. That's all you have to do.

Now remember, I said to leave the silver Pro's power switch in the on state? This is why, whenever you power up the unit, you will force the Silver Pro to complete a water test on the first run. But after the first run and entering the second it is expecting you to have a seeded batch running. Therefor it will not perform the water test again.

Just pop your next seeded batch on the stirrer and put the stopper in place connect the probes and press start, you will instantly start, no water test involved.

If however you did turn the power off, then you will have to complete the water test again. But this time you will fail the water test, why? You are starting with a seeded batch this time, its ppm content will be far greater than the Silver Pro will pass off as
safe enough water to make Colloidal silver with.

To solve this, and only if you know for sure that you are starting with a seeded batch
then leave the probes disconnected and press start. The water test will begin and will
pass. Now connect the probes to the Silver Pro.

Now you have to ask yourself, why did the silver Pro reject this water, when I know it's just a seeded batch myself?

The Silver Pro is not an analyzer of any type. It checks the resistance of the water at different voltage levels and measures the current at those levels. It can't tell what kind
of contamination is in the contents, so therefor, is safe to assume that any contaminant is a bad one. (better safe than sorry)

Only if you know for sure, that you yourself personally seeded that into good clean distilled water, should you deem it OK to bypass the water test. You can still use it as stated before, just don't consume it. Spray it on molds, mildew add it to laundry and what not, even use it to wipe down counter tops.

Section Eight:

        Do's and don'ts

OK there are a few things we need to go over here. Some of it's obvious, some not.

DO: Always wipe the probes off in between batches and when you are done using it.
Just use some Kleenex or something similar, and wipe downwards only.
.999 and .9999 silver bends easily, so if you only wipe downwards with a gentle pulling motion, there is less chance to damage the probes.

DO: After completing a batch of CS and you are only making one batch, don't use it!
What's that you say? Why not? When you only make one batch you should always make 2, here’s why. After you have made the first batch and you want to use it, what will happen to the probes? I'll tell you, you will pour some of the flask and put it to use, but what happens in the flask? Now there is a big pocket of air in the flask, leaving the probes exposed to the air. This will cause them to tarnish and be very difficult to clean off.

One way to avoid this is to make a second batch and keep the probes in the second batch, while you use the first batch. This way the probes don't get tarnished, as soon as you use the first batch make another as soon as possible.

I personally have four flasks that I keep full at all times, and two wine bottles on top of that too.

Don't: disassemble johnny five ! (please don't take this unit apart) it's very difficult to re- assemble it.

Don't: get the unit wet. (it's not a submarine)

Section Nine:

        Miscellaneous

Using mode 4:

Mode four was added for the reasoning that in some instances, you may not be able
to get the probes that you need, or that you may want to change the setup you currently are using.

An example of this would be, maybe you want to make very large batches of CS.
Lets say 5 or maybe 50 gallons at a time. If you used the normal probes,
this would take a very long time to do.

With mode 4, you can control the current, up to 1.5 amps of current! This would require some pretty big probes, or multiple probes placed in parallel.

Mode four will let you accomplish this with ease. The Silver Pro does not have a current meter built into the unit, so you will need a meter to set the current correctly.

You would just press the mode button until mode 4 led is lit. insert you meter into the circuit (probe circuit) and then press start. Let it complete the water test and start running. Depending on how much you are making, and the sizes of the probes involved, this may take a bit to get set up.

Press and hold the current button, while holding the current button rotate the front
panel 10 turn potentiometer while watching the meter. When you get to your desired
current flow, release the current button and the Silver Pro will hold that value.

If you can't get the current flow at a high enough setting, you will have to wait for the ppm content to increase enough to draw that amount of current.

Once you have the current set where you would like, you can adjust the front panel
potentiometer to set you parts per million setting.

The Silver Pro will not remember the current setting that you had used the last time, on power up it will be set for a default value. Just remember or write down the value on the potentiometer. And the next time you power it up, just hold the current button (while in mode 4) and set it for that value again. Then set your ppm setting again.

This takes very little time to complete.

Section Nine:

        Miscellaneous

Parts per million setting:

This set by the front panel potentiometer, this is active at all times and is changeable on the fly. Just rotate the potentiometer on the front panel to change the desired ppm content of the solution.

This will require some toying with and will change with different probe setups. So it can't be hard coded into the MCU to say the the value of 50 on the potentiometer is going to be 50 ppm of cs solution.

This is why I recommend getting the Hanna PWT. One you have made a few batches
with the probes that you are going to use, just keep increasing the value on the potentiometer until The Silver Pro shuts down at your required ppm setting.

And as long as you are using the same probes from batch to batch, it will always be
very accurate. ( within 1 ppm )

I you change you setup, different probes etc., then you will have to play around some more to get it set again. Just start out with the last known value and go from there.
Chances are that it won't be far off.

That's it,

Enjoy your Silver Pro, may it bring you and you family good health.